## Slide 1
ALLOTROPE
Vietnam TOU 2026 TOU Analysis V2
Updated deck from the Phase 5/6 tariff impact report
Emivest and Ecoplexus case review
May 2026

## Slide 2
Executive Summary
Updated TOU presentation regenerated with the refreshed present skill guidance.
Worst revenue hit: Emivest Bundled Discount moved by -$63,305 (-11.26%).
Best preserved case: Fixed EVN PPA kept Emivest nearly flat at -$6,076 (-1.08%).
Largest upside: Ecoplexus 40MW DPPA gained +$1,348,006 revenue and +$11.8M NPV.
Core mechanism: the tariff removed the morning peak and collapsed BESS from two cycles to one.
-$63,305
Worst Revenue Move
$1,348,006
Ecoplexus Revenue Gain
9.31%
New Ecoplexus Project IRR
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 3
01
Tariff Shift and Operating Logic
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 4
Tariff Change Summary
The five-hour peak window moved entirely into the evening, removing morning solar coincidence.
Attribute | Old (<= Apr 21) | New (>= Apr 22)
Off-Peak (Mon-Sat) | 22:00-04:00 | 00:00-06:00
Normal (Mon-Sat) | 04:00-09:30, 11:30-17:00, 20:00-22:00 | 06:00-17:30, 22:30-24:00
Peak (Mon-Sat) | 09:30-11:30 and 17:00-20:00 | 17:30-22:30
Sunday | Normal 04:00-22:00 / Off-Peak 22:00-04:00 | Normal 06:00-24:00 / Off-Peak 00:00-06:00
BESS cycles/day | 2 | 1
Lost
Morning Peak Solar Uplift
2 -> 1
BESS Cycles Per Day
17:30-22:30
Single Peak Block
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 5
Dispatch Implications
The economic loss is driven by shape, not by a uniform rate cut.
Old schedule
• Charge in off-peak 22:00-04:00
• Morning peak captured solar plus a first battery discharge
• Midday recharge enabled a second evening cycle
• Value stack combined solar timing and battery arbitrage
New schedule
• Solar from 06:00-17:30 is now fully normal-priced
• Storage value concentrates in one evening discharge window
• State-of-charge preservation matters more than cycle count
• PV-heavy structures lose more value than fixed-price offtake structures
Bottom line: the tariff change rewards evening alignment and penalizes structures that relied on morning solar uplift.
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 6
02
Case-Level Financial Outcomes
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 7
Emivest Outcome by PPA Structure
All four options start from $562,144 old-tariff revenue.
PPA Option | New Rev | Delta Rev | Delta IRR | Delta NPV
Bundled Discount | $498,839 | -$63,305 | -3.25 pp | -$659,445
Separate PV+BESS | $525,804 | -$36,341 | -1.70 pp | -$323,683
DPPA (CfD) | $542,467 | -$19,677 | -0.76 pp | -$116,188
Fixed EVN PPA | $556,068 | -$6,076 | +0.00 pp | $53,174
-$63,305
Worst Hit: Bundled
-$6,076
Best Preserved: Fixed PPA
1.64x
Lowest New DSCR
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 8
Ecoplexus 40MW DPPA Upside
Ecoplexus benefits because the new evening peak better aligns with its larger solar plus storage profile.
Metric | Old | New | Delta
Year 1 Revenue | $5,543,642 | $6,891,647 | $1,348,006
Project IRR | 6.26% | 9.31% | +3.05 pp
Equity IRR | 5.71% | 8.70% | +2.99 pp
NPV | $6,009,427 | $17,808,162 | $11,798,735
Min DSCR | 1.28x | 1.27x | -0.01x
9.31%
New Project IRR
$11,798,735
NPV Gain
+24.32%
Revenue Uplift
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 9
03
Driver Breakdown and Actions
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 10
Revenue Driver Decomposition
Bundled Discount at Emivest isolates the commercial effect of the tariff shift most clearly.
Driver | Impact | Interpretation
Loss of morning peak uplift | -$65,343 | Solar no longer lands in a morning peak block.
BESS cycle reduction | -$32,609 | One peak cycle removes half of the old arbitrage rhythm.
Shifted peak window | $34,640 | Later discharge better aligns with evening load.
Off-peak rate changes | $7 | Minimal impact in this case.
Primary conclusion: most of the downside comes from the removal of the morning peak block, partly offset by improved evening timing.
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation

## Slide 11
Recommended Actions
Commercial repricing and dispatch retuning should move together.
Re-price bundled and DPPA offers against the lower evening-only uplift.
Re-tune BESS dispatch to preserve state of charge until the evening peak.
Separate PV-heavy and BESS-heavy commercial structures when updating discounts.
Keep both tariff baselines in regression artifacts until the 2026 schedule is the default.
-11.26%
Emivest Worst Revenue Move
-1.08%
Fixed PPA Revenue Move
+24.32%
Ecoplexus Revenue Move
Confidential - For Internal Use by Allotrope & Key Partners - Not for Further Circulation